SIXTH FRAMEWORK PROGRAMME

Sustainable Energy Systems

NETWORK OF EXCELLENCE

#### Contract No SES6-CT-2004-502630

#### Safety of Hydrogen as an Energy Carrier

List of CFD models included in verification procedure
and corresponding basic test problems

Deliverable 75

Lead Participant:		FZK (A. Kotchourko)

Partners Contributing:		All contributing partner organisation

Dissemination Level: 		RE

Document Version:	Draft 0.1

Date of submission:	02.03.2007

Due date of delivery:	01.02.2007

Co-funded by the European Commission within the Sixth Framework Programme (2002-2006)

Proposal for substantial model list and several corresponding test cases

Zh. Xu

Research Center Karlsruhe

General considerations

Operation environment

Gravity

- natural circulation problem cited from literature, as shown in figure

- Hot bubble, light gas bubble

Boussinesq model

Solution strategy

Max Courant number

Convergence control

Accuracy

Governing equations

Fluid dynamics

Turbulence equations

Energy equation

- thermal equilibrium problem in a closed adiabatic cube of stagnant airs with different initial temperatures, the balance temperature can be checked.

- thermal conduct problem in an infinite plane in a thickness with different temperatures at both sides, the heat fluxes at the surface and the temperature field can be checked.

- adiabatic expansion in a closed rectangular channel, and adiabatic compression in a rectangular channel with one closed end and a moving pressure boundary on other end

- isothermal expansion and compression can be designed in 3D channels

Grid

Sensitivity on cell aspect ratio, cell size

- uniformed flow in a 2D channel with no-slip or rough wall boundary, observe the velocity profiles at the length of 15 times of diameter, different aspect ratios, sizes of cells are be used.

- 3D pipe flow, check the same things as last case.

Boundary conditions

Flow inlet / outlet

Pressure inlet, velocity inlet, mass flow inlet, inlet vent, intake fan

Pressure outlet, pressure far-field, outflow, outlet vent, exhaust fan

External boundaries

Wall, symmetry, periodic, axis

Internal face boundaries

Fan, radiator, porous jump, wall, interior

Solver

Explicit / Implicit (1st  or 2nd order)

Steady / Unsteady

2D / 3D

Isotropy in space

- heat and mass diffusion from a point in a free space (sufficiently big geometry)

- transmission of a pressure pulse

Diffusion

- 1D, 2D and 3D mass diffusion in a free space

- 1D, 2D and 3D thermal diffusion in a free space

Advection

- Boundary value problems of nitrogen diffusing into advective air flows in 1D, 2D and 3D

- Nitrogen point source released into a free advective air flows in 1D, 2D and 3D

Multiphase

Continuous phase

Discrete phase

Particle

Drag law

Particle shape

Potential force

- particle diffusion from point / line / area / volume sources into 1D / 2D / 3D advective air flows

- continuous / instantaneous particle source problems

Droplet

Collision

Breakup

Liquid surface / film

Condensation

Vaporization

Moving liquid film

Radiation

Rosseland radiation model

P-1 radiation model

Discrete transfer radiation model

Surface-to-surface radiation model

Viscosity

Inviscid

Laminar

Turbulence model

k-ε model

- isotropy uniformed turbulence decay in a horizontal rectangular channel

k-ω model

three-equations and others including more equations models

Large eddy simulation (LES)

Direct numerical simulation (DNS)

Multi-component

Species transport

Non-premixed combustion

Premixed combustion

Turbulent chemistry model

Laminar flame

Complete combustion

Chemical equilibrium

Deflagration

Detonation

Shock wave

Backward step

Decay of discontinuity (Riemann problem)

Sedov solution

Acoustics

Solidification and Melting